## Slide 2: Studs overview
Monocoque to engine studs
Engine to bellhousing studs

## Slide 3: Load cases
Monocoque to engine studs
Engine to bellhousing studs

## Slide 4: Required axial load computation
Required axial load calculation
Monocoque to engine studs
Engine to bellhousing studs
Max: 37000 N
Max: 43000 N
2.8 monocoque
2 bellhousing

## Slide 5: Thread data

## Slide 6: Tightening torque calculation
Monocoque to engine studs: 89 Nm
Engine to bellhousing studs: 78 Nm

## Slide 7: Members compliances
Stud
Clamped elements

## Slide 8: External load repartition
Monocoque to engine studs
Peak tensile load: 29015 N
Load on clamped elements: 26309 N
Load on stud: 2706 N
Engine to bellhousing studs
Peak tensile load: 21240 N
Load on clamped elements: 15641 N
Load on stud: 5599 N

## Slide 9: Stud safety factors
Monocoque to engine studs
Operation SF: 2.1
Tightening SF: 1.6
Engine to bellhousing studs
Operation SF: 2.3
Tightening SF: 1.9
Operation SF
Loads: axial preload + peak external tensile load + torque from thread friction
Minimum section
Tightening SF
Loads: axial preload + tightening torque
Root section

## Slide 10: Loosening verification
Clamped members preload reduction due to external loads
Torque wrench precision
Minimum acceptable axial preload
Monocoque to engine studs
Flim = 15377 N
Fv min = 16571
Engine to bellhousing studs
Flim = 18465 N
Fv min = 21127

## Slide 11: Xtrac reference

## Slide 12: Conclusions
Monocoque to engine studs
  90 Nm tightening torque
  Lubricated threads during installation
  If above 90 Nm, the operation SF goes below 2
Engine to bellhousing studs
  80 Nm tightening torque
  Lubricated threads during installation
  90 Nm possible
  If above 90 Nm, the operation SF goes below 2